## Slide 1: ArgosNet A Multi-Cell Many-Antenna MU-MIMO Platform
Clayton Shepard Rahman Doost-Mohammady Jian Ding Ryan Guerra Lin Zhong

## Slide 2: Argos Many-Antenna MU-MIMO Platforms
Notes: I am a systems engineer – I started building Massive MIMO systems 5 years ago.
Dr. Treichler missed “massive MIMO”. Which is also just now becoming economically viable.
We say many-antenna MIMO because our results apply to everything from relatively small systems to “massive” systems

## Slide 3: ArgosV3 An Efficient Many-Antenna Platform
Notes: And scalable physical design

## Slide 4: Argos Base Station Architecture
Central Controller
Argos Hub
Argos Hub
Argos Hub
Module
Module
Module
Module
Module
…
…
…
Data Backhaul
Module
Radio
Radio
Radio
…
Notes: Modular
  Daisy-chainable
  1 or more radios
Hierarchal
  Increases Reliability
  Constrains Latency
  Cost-effective
Replace figure w/ paper veresion?
Need a lot more here – present central controller, explain hub, etc.
Scalable in 4 directions:
  # of Radios per Module
  # of Modules per Chain
  # of ports per Hub
  # of Hubs (and levels)
Reliable
  Branches can fail without affecting other branches
  Central hubs can be easily made redundant
Accommodates linear pre-coding
  Add samples together at every junction

## Slide 6: ArgosV3 Iris Radio Modules
Lime LMS7002
  2x 50 MHz to 3.8 GHz
  58 MHz Bandwidth
Modular RF Frontend
Xilinx Zynq 7030
PoE
Large-Array Support

## Slide 7: Iris RF Frontends
UHF
  470 to 700 MHz
  30 dBm
BRS/CBRS
  2. 48 to 2.7 and 3.55 to 3.7 GHz
  28 dBm
Development

## Slide 8: ArgosV3 Mobile
~12 Hour Battery Life
Integrated GPS
Integrated WiFi

## Slide 9: ArgosV3 Hub
8 Chains of Irises
160 Radios
Xilinx ZCU102
Integrated GPS
SyncE/PTP (NGFI)
Scale with Multiple Hubs
Notes: 2,520 DSPs

## Slide 10: ArgosV3 Base Station Implementation

## Slide 11
Notes: Custom antenna array
~60 Lbs

## Slide 14: Why Multi-Cell Massive MIMO?
Reduced Inter-Cell Interference
CoMP
Pilot Contamination
Other Research
Notes: At scale, tomography, localization, architecture, etc.
Drones

## Slide 15
Notes: 5 locations, 2 with 2 sets of fibers/mounts
40 2-antenna UEs

## Slide 22: ArgosNet Architecture
208-Core Cloud
ZCU102 with 12 SFP+
4x 10 GbE
NGFI (SyncE/PTP)
CPRI

## Slide 23: Framework Support
SoapySDR/Pothos (LimeSDR)
GNU Radio (UHD Driver)
OpenAirInterface
Argos Realtime Flow

## Slide 24: Many-Antenna Measurement System
ArgosV2 --> ArgosV3
Faros
Python
  Accelerated in C
Notes: So I built a system to measure realtime wideband MU-MIMO channels.

## Slide 25: Multi-Cell Measurement System Design
ArgosCloud
IQ
IQ
User 1
Noise
User 2
…
User K
Notes: The measurement system is based on a scheduled frame, and leverages the Faros mechanisms for time-frequency synchronization with the mobiles.
The base station sends a beacon, which provides the users synchronization, then they send orthogonal pilots; in this case we use TDMA to achieve orthogonality.
After the pilot phase each base station antenna reports the raw IQ samples to the central controller, which saves them.
This happens every frame (thus the frame length is the collection interval).
In multi-cell we can’t do uplink AGC to every cell, so we have users rotate gains to get good dynamic range at every base station (sacrificing some time resolution).

## Slide 26: Everything is released online!
http://data.projectargos.org
Notes: Clean, well documented – maps photos, videos.
Includes measurements, analysis toolbox, and measurement system.

## Slide 27: ArgosNet
Fully Programmable Multi-Cell Indoor/Outdoor Long-Range Massive MIMO Platform
Enables unprecedented at-scale experimental research
Fully Programmable Multi-Cell Indoor/Outdoor Long-Range Massive MIMO Platform
Flexible Framework Support
Demonstrate incredible potential for Massive MIMO to reduce inter-cell interference and increase cell-edge performance

## Slide 28: Thank You!
Ryan Guerra
Lin Zhong
Jian Ding
Rahman
Doost-Mohammady
Notes: Thanks to my co-authors, as well as some others who helped with the measurements.